## Slide 1
mOT.sendRequest()
sOT.sendResponse()
MASTER
OpenTherm
Shield
SLAVE
OpenTherm
Shield
THERMOSTAT
MCU
BOILER
slave
master
gateway
voltage
voltage
DIG IN
DIG OUT
current
current
DIG OUT
DIG IN
sOT.handleInterrupt() processes
incoming bits and figures out sOT.status
mOT.handleInterrupt() processes
incoming bits and figures out mOT.status
#include <Arduino.h>
#include <OpenTherm.h>
OpenTherm mOT(mInPin, mOutPin); // Manages Master OpenTherm Shield
OpenTherm sOT(sInPin, sOutPin, true); // Manages Slave OpenTherm Shield
void ICACHE_RAM_ATTR mHandleInterrupt() { mOT.handleInterrupt(); }
void ICACHE_RAM_ATTR sHandleInterrupt() { sOT.handleInterrupt(); }
void processRequest(unsigned long sOT_request,
OpenThermResponseStatus sOT_status) {
// Send the intercepted thermostat request further downstream to the boiler
// and listen for the boiler's response.
unsigned long mOT_response = mOT.sendRequest(sOT_request);
if (mOT_response) {
// A boiler response is waiting to be processed. Send this intercepted
// response further upstream to the thermostat.
sOT.sendResponse(mOT_response);
}
}
void setup() {
mOT.begin(mHandleInterrupt);
sOT.begin(sHandleInterrupt, processRequest);
}
void loop() {
// Poll whether a new thermostat request awaits. `process()` will internally
// call `processRequest()` when needed.
sOT.process();
}
Code excerpt for gateway:
Schematic: DIYLESS OpenTherm shields and code flow
Dennis van Gils, 15-01-2023
processRequest()
mOT_response
sOT_request